Free space representation algorithm it1 with Frenet-frame coordinates

IN:
D(n,k) = pairs of Delta_s and Delta_ey with occupied space for each neighbour N along an	horizon H
robot model F
current position

OUT:
Set of constraints for the optimisation problem

set r(0) = real_position

for j = 1:H
1. compute reachable space from r (j-1) → r(1) = F(r(0))
2. for n = 1:N
  1. for k = 1:H
    1. box = r(1)\D(n,k)
3. r(1) = Intersection of all boxes → resulting intervals are the free space at time k

Problems:
- We are not using temporal information in the plans
- Computationally migh be costly for a high number of robots / Horizon

Proof of concept: function it1

Status: Discarded as the exclusion operator scales very badly the problem, for instance first time we split the world we generate four intervals that need to be acounted for.

Ideas/lines that we could follow to improve

- Use another type of operator, like write it as some kind of constraint
- Use another type of set theory
- Don’t try to represent the free space using all reachable space, only some heuristics from previous MPC
- add temporal relationship to only use samples once (each robot can only be in one position at a time)

Free space representation algorithm it2 with Frenet-frame coordinates

IN:
D(n,k) = pairs of Delta_s and Delta_ey with occupied space for each neighbour N along an	horizon H
robot model F
current position

OUT:
Set of constraints for the optimisation problem

Motivation: Coming from the previous iteration I want to try to write similar to forward-backward SIVIA so that the output of the algorithm are the minimum boxes at each time step.

ee space representation algorithm it2 with Frenet-frame coordinates

IN:
D(n,k) = pairs of Delta_s and Delta_ey with occupied space for each neighbour N along an	horizon H (keep in mind we need to reference them wrt )
robot model F
current position

OUT:
Set of constraints for the optimisation problem

Motivation: Try to expand the naive obstacle avoidance that Eugenio used in his paper.

1. Estimate a maximum reachable S → Sr
2. Stablish a step size to discritise S → either using the previous prediction or
3. for j = s_0; j+=ds; Sr
  1. Search for the closest obstacle to the right
  2. Search for the closest possible obstable to the left

PROS

- We are finding the biggest connected corridor around the upcomign S.
- Relatively simple to implemetn

TODOS
- We need to make something to make the search in an inteligent manner, otherwise we will have to compute distance at each time step with NxH regions → ordening in terms of S and Ey so that we rapidly find the first one?
- Which distance metric is the best to asses the closest region? → search the most restrictive region around current s

CURRENT STATE
the minimum example is functional, however without many samples it takes around 5ms, may be improvable by “discretising” the limits in more realisitc timeframe (rn working with a very small steps)